## Slide 1: QUIC
Geoff Huston AM
APNIC

## Slide 2: TCP is..
The workhorse of the Internet!
A transport protocol that constructs a reliable full duplex adaptive streaming service on top of an unreliable IP datagram service
  Uses a coordinated state between the two end systems without any network intervention or mediation
  Uses a sliding window to allow lost data to be resent
  Uses ACK-clocking to regulate the sending behaviour to match network path capacity estimate

## Slide 3: TCP is NOT…
Fully independent of the underlying platform Operating System’s transport services
Fully multi-stream (it has head-of-line blocking)
Fully multi-path (yes, MP-TCP exists, but there are some outstanding issues here!)
Address-agile
Free from on-the-wire network intervention (TCP control parameters are sent in the clear)
Has e2e encryption as a second step / afterthought (TLS)
Everything for everyone – it relies on the application to perform data framing and in-band control

## Slide 4: QUIC is a mashup of TCP and TLS
HTTP
Multi-stream
TLS
Session Encryption
TCP
Data stream integrity
Congestion Control
HTTP
QUIC
Multi-stream
Encryption
Data stream integrity
Congestion Control
UDP
IP
HTTP/2
QUIC
HTTP/3
e2e encrypted
e2e encrypted

## Slide 5: QUIC is…
Constructed upon a basic UDP datagram service
  All other transport services (data integrity, session control, congestion control, encryption) are shifted upwards in the protocol stack towards the application. A host platform may provide a QUIC API as part of the host library, but the application can also provide its own QUIC service independent of the host

## Slide 6: QUIC is…
So much more than just “encrypted TCP over UDP”
  Support for multi-stream multiplexing that avoids head-of-line blocking and exploits a shared congestion and encryption state
  Faster - Combines transport and encryption setup exchange in a single 3-way exchange at session start, and supports fast reopen
  Customisable - QUIC implementations can use individual flow controllers
  QUIC places its transport control fields inside the encryption envelope using TLS 1.3, so QUIC features minimal exposure to the network
  Supports Remote Procedure Call service models as well as bit-streaming and datagram services

## Slide 7: QUIC is address agile
NATs are potentially hostile to QUIC because of the outer UDP wrapper
  A NAT may rebind a QUIC session (shift the externally visible address/port of a host during a session), as NATs are not generally aware of UDP streaming states
QUIC uses a persistent “connection ID”
  If a host receives a QUIC frame with the same connection ID and a new source IP address / port it will send a challenge by way of a random value that should be echoed back. This is all performed within the e2e encryption envelope. That way a QUIC e2e session can map into new address/port associations on the fly

## Slide 8: QUIC also…
Is IP fragmentation intolerant – QUIC uses PMTUD, or defaults to 1,200 octet UDP payloads
Never retransmits a QUIC packet – retransmitted data is sent in the next QUIC packet number – this avoids ambiguity about packet retransmission
Extends TCP SACK to 256 packet number ranges (up from 3 in TCP SACK)
Separately encrypts each QUIC packet – no inter-packet dependencies on decryption
May load multiple QUIC packets in a single UDP frame

## Slide 9: QUIC flow structuring
A QUIC connection is broken into “streams” which are reliable data flows – each stream performs stream-based loss recovery, congestion control, and relative stream scheduling for bandwidth allocation
QUIC also supports unreliable encrypted datagram delivery

## Slide 10: QUIC is:
A logical evolutionary step for transport services, providing more flexibility, faster connection setup, and a larger set of transport services
It’s what we should expect from a capable modern transport protocol!

## Slide 11: But…

## Slide 12: QUIC and Network Load Balancing
Front-end load balances performing load balancing on UDP flows using the UDP connection 5-tuple
If the remote end performs NAT rebinding the load balancer will be thrown by this shift, and it has no direct visibility into the e2e session to uncover the connection ID
NAT
Load Balancer
Server A
Server B
Source Address A
Source Address B
NAT re-binding
QUIC session

## Slide 13: QUIC and Network Load Balancing
Front-end load balances performing load balancing on UDP flows using the UDP connection 5-tuple
If the remote end performs NAT rebinding the load balancer will be thrown by this shift, and it has no direct visibility into the e2e session to uncover the connection ID
If we really want large scale QUIC with front-end load balancing and if we still need to tolerate NATs then we will need to think about how the end point can share the connection ID state with its front-end load balancer, or how to terminate the QUIC session in the front-end and use a second session to a selected server

## Slide 14: QUIC and NIC Offloading
Many (most?) NICs these days offer ”TCP Offloading”
  Platform sends a large data buffer to the NIC, and the processor in the NIC performs TCP segmentation
  The NIC reassembles smaller received data units to a larger unit before raising an interrupt to the host processor
  Relieves the CPU from TCP processing overheads, improving server capacity
Offloading QUIC to NICs is work-in-progress
  But its looking good – QUIC is well suited to device offload
  There is a need for mods to kernel and network drives, as well as QUIC libraries
  It’s not here just yet, but it is looking promising!

## Slide 15: Measuring QUIC

## Slide 16: Triggering QUIC in HTTP
Use the DNS to trigger QUIC:
  Set up an HTTPS record for each server name, with value: alpn=“h3”
Use content-level controls to trigger QUIC:
  Add Alt-Svc: h3=“:443” to the HTML headers
  (This second method requires a subsequent query in a distinct HTTP session to allow the client to use the Alt-Svc capability.)

## Slide 17: Setting Expectations
Chrome has a dominant share of browser instances - roughly, some 65%*
And Chrome has been supporting a switch to QUIC via the Alt-Svc directive since 2020
* Oberlo.com

## Slide 18: Setting Expectations
Chrome has a dominant share of browser instances - roughly, some 65%*
And Chrome has been supporting a switch to QUIC via the Alt-Svc directive since 2020
And Apple Safari is now supporting QUIC, using the DNS apln directive
So a QUIC-aware server platform should be seeing some 85% of its sessions using QUIC – right?
* https://gs.statcounter.com/browser-market-share

## Slide 19: Cloudflare’s Numbers

## Slide 20: APNIC’s Numbers
Playing with keepalive parameters!
First Fetch – mainly Safari clients
Second and Subsequent Fetches – mainly Chrome clients

## Slide 21: APNIC Measured QUIC Use – September 2024
100%

## Slide 22: Network Traffic Volume
Presentation to RIPE 86: The New Encrypted Protocol Stack and How to Deal with it – Bart van de Velde, Cisco

## Slide 23: Why is QUIC important?
Because QUIC is fast
Because QUIC encrypts everything
  No visible transport control settings
  No visible Server Name Indication in the crypto-setup
  No visible traffic profile other than inter-packet timing
  And if you use a MASQUE-based VPN then there no residual visibility!

## Slide 24: What does this mean for TCP?
It’s not looking all that good for TCP’s prospects
QUIC not only does faster start up, but it supports multi-channel in a frictionless manner
QUIC resists network operator efforts to perform traffic shaping through direct manipulation of TCP control parameters
QUIC allows the application service provider to control the congestion behaviour of its sessions

## Slide 25: What does this mean for TCP?
Normally you would expect any transition from TCP to QUIC to take forever
BUT:
QUIC gives benefit to adopters through more responsive web services
QUIC does a better job of hiding content, which is a benefit to the service operator
QUIC has fewer external dependencies
QUIC can be deployed on a piecemeal basis
So it all may be over for TCP in a very small number of years!

## Slide 26: What does this mean for the Internet?
IP was a network protocol that provided services to attached devices
The network service model used by IP was minimal
  Packets may be dropped, fragmented, duplicated, corrupted and/or reordered on their path through the network
  It’s left to the edge systems to recover from this network behaviour.
Efforts to expand the network’s role have foundered
  QoS has just got nowhere!
  Various forms of source-directed forwarding are resisted by network operators who want control over traffic engineering
media
network
TCP Transport
apps
$$$

## Slide 27: The new Networking Space
And this is why QUIC is so interesting – it is pushing both network carriage and host platform into commodity roles in networking and allowing applications to effectively customize the way in which they want to deliver services and dominating the entire networked environment
QUIC is the application’s view of what Transport should be!
media
network
TCP Transport
apps
media
network
UDP Transport
apps
Internal
Transport +
session security
$$$
QUIC and value transform
in the network stack

## Slide 28: What does this mean for the Internet?
The relationship between applications, hosts and networks has soured into mutual distrust and suspicion
The application now defends its integrity by wrapping up as much of the service transaction with encryption and indirection
QUIC (and MASQUE) is an intrinsic part of this process of wrapping up traffic in encryption and redirection
For the network operator there is little left to see
And I suspect that there is no coming back from here!

## Slide 29: What can a Network Operator Do?
When all customer traffic is completely obscured and encrypted?
  Traffic Shaping?
  Regulatory Requirements for traffic interception?
  Load Balancing / ECMP

## Slide 30: The new Internet Space
“What you can’t dominate, you commoditise*”
Vertically integrated service providers have faded away into history - the deregulated competitive service industry continues to specialize rather than generalize at every level
Carriage is no longer an inescapable monopoly - massively replicated content can be used as a substitute for many carriage service elements
Control over the platform is no longer control over the user. Operating systems have been pushed back into a basic task scheduling role, while functions are being absorbed into the application space
* A related quote is Peter Thiel’s “Competition is for losers!”

## Slide 31: Thanks!